## Slide 2: Objectives
To understand the purpose of various four-stroke engine components.
To determine the purpose and types of cooling systems in four-stroke engines.
To understand the uses and importance of engine oil.
To analyze lubrication systems in four-stroke engines.

## Slide 3: Main Menu
Engine Components
Engine Cooling
Engine Oil & Lubrication Systems

## Slide 4
ENGINE COMPONENTS

## Slide 5: Four-Stroke Engines
Are composed of many components, including:
  piston
  piston rings
  wrist pin or piston pin
  connecting rod
  crankshaft
  camshaft
  lifters
  valves

## Slide 6: Four-Stroke Engine
2
1
3
4
5
6
7
Piston
Piston Rings
Wrist Pin/Piston Pin
Wrist Pin/Piston Pin Retaining Clip
Connecting Rod
Crankshaft
Connecting Rod Cap

## Slide 7: Four-Stroke Engine
Oil Dipper
Camshaft
Lifters
Pushrods
Rocker Arms
Valve Springs
Valves
12
9
8
11
14
13
10

## Slide 8: Piston
Travels within the bore of the cylinder
Transfers combustion energy to the crankshaft
Four-Stroke Fact: The cylinder wall and the piston expand at different rates, so enough clearance must be provided between them.

## Slide 9: Piston Rings
Are installed on the piston to form a seal between the piston and the cylinder wall
Are typically made of high-grade cast iron and steel
Have the following functions:
  provide a seal to hold the combustion pressure in
  retain as much oil as possible in the crankcase
  transfer heat from the piston to the cylinder walls

## Slide 10: Piston Rings
Include three common types:
  compression ring
  scraper/wiper ring
  oil control ring

## Slide 11: Compression Ring
Is installed in the top groove on the piston
Provides the seal for the cylinder by expanding out against the cylinder wall
  the compression pressure will flow in behind the compression ring to increase pressure against the cylinder wall
Is typically made of cast iron

## Slide 12: Scraper/Wiper Ring
Is located between the compression ring and the oil ring
Is used to further seal the combustion chamber and wipe the cylinder wall clean of excess oil

## Slide 13: Oil Control Ring
Is located in the groove closest to the crankcase
  toward the bottom
Wipes excess oil from the cylinder wall and routes the oil back to the crankcase
  the oil goes back to the crankcase through holes machined in the ring and the piston ring groove

## Slide 14: Wrist Pin/Piston Pin
Attaches the piston to the upper end of the connecting rod
Allows the piston to pivot on the end of the connecting rod
  while the other end of the connecting rod is following the stroke of the crankshaft
Can be pressed in or held in place by a wrist pin retaining clip at each end

## Slide 15: Connecting Rod
Connects the piston to the crankshaft
  the small end is attached to the piston with the wrist pin
  the large end is usually split across the diameter of its opening to allow for assembly onto the crankshaft
Four-Stroke Fact: The reciprocating movement of the piston in the cylinder is converted to the rotational movement of the crankshaft.

## Slide 16: Connecting Rod
Connects the piston to the crankshaft
  the lower half of the large end is the connecting rod cap and is bolted to the upper half after placing it around the connecting rod journal on the crankshaft
Four-Stroke Fact: The connecting rod and its connecting rod cap are manufactured as a unit and must always be kept together.

## Slide 17: Crankshaft
Converts the reciprocating movement of the piston into a rotational movement, creating torque which powers the machine the engine is attached to
Has a mechanical link, usually gears, to the camshaft and mechanical governor
Four-Stroke Fact: The distance from the centerline of the crankshaft to the centerline of the connecting rod journal, multiplied by two, determines the stroke of the engine.

## Slide 18: Camshaft
Is at half speed of the crankshaft, usually through direct gear contact
Will have a teardrop lobe to open each intake and exhaust valve
Determines the timing when valves open and close in relation to each other

## Slide 19: Lifters
Are also known as tappets
Are located on the camshaft lobes
  as the camshaft rotates, the lifter follows the profile of the camshaft lobe and moves the pushrod up and down to move the rocker arm
Include two types
  hydraulic
  mechanical

## Slide 20: Hydraulic Lifters
Have multiple parts and are usually replaced as a unit
  through the use of a spring, inner and outer cylinders, and engine oil, the hydraulic lifter will be maintenance free
Allow for constant contact between the cam, lifter, pushrod, rocker arm and valve

## Slide 21: Mechanical Lifters
Are solid, without moving parts
  these lifters typically require some adjustment regularly as components wear
    the most common form of adjustment is at the rocker arm
Are typically made of solid metal

## Slide 22: Valves
Are components which allow the air/fuel mixture in and exhaust out
Are made of heat resistant materials
  the exhaust valve is usually made from a separate alloy metal
Include the use of valve seats
  valve seats are inserted into the cylinder head for the valves to seal and transfer heat
  valve seats are grounded to an angle which mates with the valve face, so a tight seal is created when the valve is closed

## Slide 23: Engine Cooling
ENGINE COOLING

## Slide 24: Air-Cooled Engines
Generate heat which is released directly into the air
Rely on the circulation of air to cool hot engine components
  heat must be removed from the engine to prevent permanent damage

## Slide 25: Air-Cooled Engines
Hot Air
Shroud
Warm Air
Cool Air
Flywheel Fins
Intake Screen
1
2
3
4
5
6
5
4
3
2
1

## Slide 26: Air
Is brought in through an air intake screen by fins on the flywheel and distributed through a shroud and then across the fins on the cylinder(s)
  metal fins covering the outside of the cylinders are used to increase the surface area air can act on
  the air movement across the cooling fin draws away excess heat
Four-Stroke Fact: In all combustion engines, a great percentage of the heat generated escapes through the exhaust.

## Slide 27: Heat Energy
May find its way into the oil, which although primarily meant for lubrication, also plays a role in heat dissipation
  on an air-cooled engine, the addition of an oil cooler may greatly help in the dissipation of heat

## Slide 28: Engine Overheating
May occur if any part of the air flow is restricted by debris
May also be caused by one or more of the following:
  obstructions or blockage of air intake screen
  obstructions on or in the flywheel fins
  obstructions or damage to the shroud
  obstructions or damage to the cylinder cooling fins
  obstructions or damage to the external cooler

## Slide 29: Liquid-Cooled Engines
Utilize a radiator, coolant pump, thermostat, engine coolant passages, and the correct blend of coolant and water to regulate and dissipate engine heat
Four-Stroke Fact: Coolant, commonly called antifreeze, is a mixture of ethylene or propylene glycol and water.

## Slide 30: Liquid-Cooled Engine
Radiator
Hot Coolant
Thermostat
Coolant Pump
Cylinder Head
Coolant Passage
Cooled Coolant
Cooling Fan
1
2
3
4
5
6
7
8
4
7
8
1
2
6

## Slide 31: Liquid-Cooled Engines
Operate in the following manner:
  coolant is circulated from the coolant pump to the cylinders, engine block, cylinder head, valves and combustion chambers through a series of coolant passages
    coolant exiting the engine flows through the thermostat housing
  coolant flows through a check valve opening in the thermostat, enabling a fast warm-up period
    the check valve also acts as a vent to allow air to escape while filling the cooling system
    before engine warm-up, the thermostat is closed

## Slide 32: Liquid-Cooled Engines
Operate in the following manner:
  once the engine has reached full operating temperature, the thermostat will completely open, allowing maximum coolant flow through the upper radiator hose to the radiator top tank
  coolant circulates through the radiator, dissipates heat and flows out the lower radiator hose back to the coolant pump

## Slide 33: Excessive Temperatures
Will trigger the pressure cap to open to allow excess coolant to flow into the expansion tank
  when the coolant temperature drops, the pressure cap will close
  as the coolant continues to cool, a vacuum will form in the radiator, opening a valve in the pressure cap, allowing coolant to be siphoned from the expansion tank back into the radiator

## Slide 34: Engine Coolant
  Will continue circulating throughout the system until the coolant temperature drops below the thermostat temperature rating, at which the thermostat begins to close and the sequence starts again
Allows the engine to operate at an optimal temperature, facilitating clean, efficient operation

## Slide 35: Engine Overheating
May be caused by one or more of the following:
  improper mixture of water and coolant/antifreeze
  improper level of coolant
  improper fan belt tension
  internally clogged radiator
  externally clogged cooling fins on radiator
  thermostat opening slowly or not at all
  collapsed hoses
  faulty water pump
  blockage of water flow in the block or cylinder head

## Slide 36: Engine Oil & Lubrication Systems
ENGINE OIL & LUBRICATION SYSTEMS

## Slide 37: Pressure-Lubricated Engines
Typically utilize a wet sump lubrication system in which the oil pump is driven by the crankshaft
Four-Stroke Fact: Most systems include a pressure regulation system which maintains a working pressure.

## Slide 38: Pressure Lubrication System
1
2
3
4
5
8
7
6
Crankshaft Journal Oil Passage
Camshaft Oil Passage
Main Bearing Oil Passage
Oil Filter
Oil from Sump
Pickup Strainer
Oil Pump
Crankshaft

## Slide 39: Pressure-Lubricated Engines
Operate in the following manner:
  the rotation of the oil pump draws oil from the sump through the pickup strainer
    the sump is the lowest part of the engine
  the oil is pumped into passages in the engine block, which route the oil to the components requiring lubrication
    oil is routed to bearings, bushings, hydraulic lifters and rotating crankshaft assembly

## Slide 40: Oil Pressure Switch
Is situated in an engine block oil passage
Alerts the operator of a low pressure situation
  the engine oil continues to a full-flow oil filter equipped with a bypass valve
    if oil flow through the filter becomes restricted, the bypass valve opens to allow engine oil to continue to circulate through the engine

## Slide 41: Splash Lubrication System
Uses an oil dipper, attached to the connecting rod cap in a horizontal-crankshaft engine
Four-Stroke Fact: In a vertical-crankshaft model, the oil dipper will be attached to a crankshaft counterweight, or it will be a separate component driven by the cam gear.

## Slide 42: Splash Lubrication
Direction of Rotation
Crankshaft
Connecting Rod Cap
Oil Dipper
Oil Supply
Crankcase
1
2
3
5
6
4

## Slide 43: Splash Lubrication System
Operates in the following manner:
  with each rotation of the crankshaft, the oil dipper reaches into the engine’s oil supply like a small cup at the bottom of the crankcase, throwing oil onto the internal engine parts

## Slide 44: Engine Oil
Is used in the lubrication system to perform the following four basic functions:
  lubrication
  sealing
  cooling
  cleaning

## Slide 45: Choosing the Correct Oil
Requires technicians to know how lubricating oils are rated
  the oil should meet the manufacturer’s viscosity recommendations and performance classification
Four-Stroke Fact: By law, a manufacturer cannot require users to run their oil. The manufacturer can only specify the specific oil quantity and grade.
Viscosity – resistance to flow

## Slide 46: Choosing the Correct Oil
Can be accomplished with the help of the American Petroleum Institute (API) and Society of Automotive Engineers (SAE) standards

## Slide 47: API & SAE
Are voluntary collaborations of the automotive and oil industries to ensure certain standards
Place a symbol on oil containers which gives technicians consistent standards of information among oil brands and formulations
  a container of engine oil bearing the API and SAE symbols conforms to the standards and specifications of each

## Slide 48: API & SAE Symbols
Contain information about the following:
  viscosity grade
  oil performance classification
  energy conservation rating

## Slide 49: Oil Ratings
Include API ratings which are expressed as C for compression ignition and S for spark ignition
  also includes codes which indicate the use of the oil in a certain engine
Include SAE ratings to ensure the standards of the oil’s viscosity
  a multi-viscosity oil is commonly recommended

## Slide 50: Crankcase Breather System
Is required to maintain a net-negative pressure in the crankcase
  a net-negative (vacuum) is necessary to control oil consumption and manage crankcase vapor for emissions concerns
Four-Stroke Fact: Modern engines incorporate a closed crankcase breather system.

## Slide 51: Resources
The Equipment & Engine Training Council Four-Stroke Education Committee (2016) Four-Stroke Study Guide
http://courses.washington.edu/engr100/Section_Wei/engine/UofWindsorManual/Piston%20and%20Piston%20Rings.htm

## Slide 52: Acknowledgments
CEV Multimedia, Ltd.
©MMXVII
Assistant Brand Manager
Stevi Huffaker
Graphic Designer
Melody Rowell
Quality Control Director
Angela Dehls
V.P. of Brand Management
Clayton Franklin
Special Thanks
The Equipment & Engine
Training Council
Executive Producer
Gordon W. Davis, Ph.D.